OTHR Risk Register

Document Status

| Version | Date | Revision | Prepared | Reviewed | Approved |
| --- | --- | --- | --- | --- | --- |
| A | 16th May 2016 |  | Ian Davis | PR,ID | Mngnt Committee |

Revision Record

| Revision | Date Issued: | Description of change: |
| --- | --- | --- |

Oberon Tarana Heritage Railway Risk Register

| Risk No | Category | Risk/hazard Description | L’hd | cons | Risk Class | Control Measures | Expected Outcomes | Resid L’hd | Resid Cons | Resid Risk | Risk Owner |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Competency | No formal training to work in the railway danger zone Injury/death | 2 | 3 | 5 | Track work will be carried out under the supervision of track maintenance personnel who hold a current Certificate II in Transport and Logistics (Railway Infrastructure) All member of the team undertaking track work must hold a current OTHR safety Induction Ensure all controls are in place and where appropriate compliance with relevant standards | No injury/death | 1 | 2 | 3 | Track Manager |
| 2 | Drug and Alcohol | Under the influence of Drugs and Alcohol A danger to self, others and infrastructure. | 2 | 3 | 5 | All personnel undertaking track work have read and understood the OTHR Drug and Alcohol Policy. All members to be aware of this risk and if someone is believed to be affected request the affected person to not undertake the duty and report it to the supervisor | Ensure all controls are in place and where appropriate compliance with relevant standards | 2 | 1 | 3 | Track Manager |
| 3 | Fatigue | Affected by Fatigue A danger to self, others and infrastructure. | 3 | 3 | 6 | All personnel undertaking track work have read and understood the OTHR Fatigue Policy. All members to be aware of this risk and if someone is believed to be affected request the affected person to not undertake the duty and report it to the supervisor.. | Ensure all controls are in place and where appropriate compliance with relevant standards | 2 | 2 | 4 | Track Manager |
| 4 | Safe Working | Protecting self from injury and dangers Protecting self from injury and dangers Dangers from working within the rail danger zone | 3 | 4 | 7 | Instruction, Information, Training and Supervision Workplace hazard identification/ Specific task instructions Plant safety procedures - planned maintenance programs, daily safety checks, regular safety inspections Employee safety rules/responsibilities; All personnel undertaking track work have read, understood and signed the Induction Booklet If you have medical condition that would affect your work inform supervisor before you start. Have the correct (and wear correctly) the following Personnel Protective Equipment: Hi Visibility Orange Safety Vest Boots Hard Hat Gloves Safety glasses Ear protection ) Sunscreen Drinking water available One member of the team to have a two way radio or mobile phone Keep clean water on site in case of burns Mitigation of safety breaches by supervision | No injury/death Ensure all controls are in place and where appropriate compliance with relevant standards | 2 | 2 | 4 | Track Manager |
| 5 | OHS compliance | Working alone Injury/death | 3 | 3 | 6 | No one is permitted to work alone within the rail danger zone. OTHR has a teaming system for all track work. | No injury/death | 1 | 2 | 3 | Track Manager |
| 6 | Track Access | Ensuring workers have correct possession of the track Injury/death | 3 | 4 | 7 | Ensure supervisor has filled in the track access log book. Red flag and witches hat is placed in the centre of the track before accessing that section. No machines are working in that section of the track. | No injury/death | 1 | 3 | 4 | Track Manager |
| 7 | Prestart safety briefing | Worksite safety Injury/death | 2 | 4 | 6 | Site safety inductions and job safety induction are completed and signed by all workers. All risks are identified and recorded. | No injury/death | 1 | 2 | 3 | Track Manager |
| 8 | Finishing Job | Worksite safety Injury/death | 2 | 4 | 6 | All workers are accounted for. All equipment and tools have been returned and stored correctly. All log books have been filled out and red flag and witches hat removed. |  | 2 | 2 | 4 | Track Manager |
| 9 | Track Machines | Railway track become unsafe for use by track machines leading to damage to vehicle, injury and/or death | 4 | 4 | 8 |  Track condition maintained as per SOP-011;  Track inspected as per F-037  Railway safety workers have the correct & current competency for any of the tasks that they are undertaking as per the General Induction Course IND006  A budget is maintained by the Management Committee to complete necessary track maintenance | No injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections | 2 | 2 | 4 | Track Manager |
| 10 | Track Machines | Rail workers being injured or killed by track machines | 3 | 5 | 8 |  All operators have the current and correct competency for the machine they are operating;  Site supervisors ensure all workers are aware of machinery operating within the rail corridor;  If necessary, worksite is fenced off to reduce the risk of workers coming in contact with the machines;  All workers have completed the OTHR Induction Course.  All machines are maintained as per the manufacturers’ requirements & OTHR maintenance policy;  All “near misses” are investigated within 14 days and include recommendations to | No injuries to persons; Random audits of competencies to show 100% of competency compliance by workers; All “near misses are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 2 | 2 | 4 | Track Manager |
| 11 | Sleepers | Sleeper failure leading to injury or death and derailment of track machines | 3 | 5 | 8 |  Sleepers are inspected as per OTHR track standards · Railway workers have the correct & current competency for tasks they are undertaking as per COM-002 | No injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections | 2 | 2 | 4 | Track Manager |
| 12 | Rail Joints | Rail joint damage or failure leading to injury or death | 1 | 4 | 5 |  Rail joints are inspected as per OTHR track standards  Railway workers have the correct & current competency for tasks they are undertaking | No injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections | 1 | 2 | 3 | Track Manager |
| 13 | Points | Points damage or failure leading to leading to injury or death | 2 | 4 | 6 |  Ensure points are inspected as per OTHR track standards  Railway workers have the correct & current competency for tasks they are undertaking | No injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections | 1 | 2 | 3 | Track Manager |
| 14 | Level Crossings | Road crossing damage or failure leading to injury or death | 2 | 4 | 6 |  Crossing are inspected as per OTHR track standards  Railway workers have the correct & current competency for tasks they are undertaking | No injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections; All “near misses are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 1 | 3 | 4 | Track Manager |
| 14 | Level Crossings | Collisions between pedestrian or car with track machines at crossings | 3 | 4 | 7 |  All operators have the correct & current competency for the machine they are operating.  All crossings have correct passive warning signs  All track machines are maintained in accordance with OTHR Maintenance Policy | No collisions with pedestrians or vehicles no injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections; All “near misses are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 2 | 3 | 5 | Track Manager |
| 15 | Track Machine Operation | Incorrect operations of Track Machines | 3 | 4 | 7 |  All operators have the correct & current competency for the machine they are operating.  All track machines are maintained in accordance with OTHR Maintenance Policy | No injuries to persons; No damage to track vehicles; No derailments; All “near misses or incidents are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 2 | 2 | 4 | Infrastructure Manager |
| 16 | Fire | Asset damage from fire within the rail corridor | 3 | 4 | 7 |  The whole rail corridor has a high risk of bushfire and it is impracticable to manage the whole line for this risk. The Incident Management Plan IM-004 provides guidelines to the Track Manager on where to focus the resources to manage the risks.  The emergency and evacuation procedure IM-004 is carried out periodically  Fire fighting equipment is correctly located and operational  All operators of all machines are halted until the track is checked and declare safe | No injuries to persons; No damage to track vehicles; No derailments; All damage is completed before normal operations can continue; All fires are promptly reported. | 2 | 2 | 4 | Infrastructure Manager |
| 17 | OH&S | Railway workers are unfit and/or unable to undertake their tasks | 3 | 3 | 6 |  All railway workers comply with OTHR health and fitness guidelines  All railway workers comply with OTHR Drug and Alcohol Policy P-004  All railway workers comply with OTHR Fatigue Management Policy P-003 | Workers are fit and able to undertake their tasks safely. | 1 | 2 | 3 | Rail Safety Manager |
| 18 | Materials | Incorrect or substandard materials used in railway infrastructure leading to damage of machines and infrastructure as well as injury and death | 3 | 4 | 7 |  New material will require quality certification from the supplier  Where second hand material is used to meet heritage requirements, they will be subject to quality inspections to confirm fitness for the intended purpose · Material purchases must comply with OTHR Purchasing Policy P-009 | No injuries to persons; No damage to track vehicles; No derailments; 100% compliance with inspections processes. | 1 | 2 | 3 | Infrastructure Manager |
| 19 | Interface | Failure to reach interface Management agreements with other rail operators, companies, organisations and individuals | 4 | 4 | 8 |  The secretary to review and update the OTHR Interface Register  The secretary and sub-committee to progress the development of interface agreements and provide the Management Committee with regular up-dates  If development of interface agreements with a risk assessment for each crossing.  If an interface agreement is not in place the Infrastructure Manager will put in place measures for locations that have a high risk to reduce these risks such as warning signs and procedures to limit the hazards.  General Public are only permitted in the OTHR Carriage Shed only when there are no repairs, maintenance or movement of any rolling stock. This must be under direct supervision at all times.  General Public are permitted in and around the Oberon Railway Station only during daylight hours or when under direct supervision for night event. Access to other parts of the Oberon Railway Station precinct is permitted for special events only when no railway operations are occurring. | No collisions with pedestrians or vehicles no injuries to persons; No damage to track vehicles; No derailments; 100% compliance with track inspections; All “near misses are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 2 | 2 | 4 | Secretary |
| 20 | Crane Use | Incorrect lifting and removing rolling stock with a crane | 3 | 4 | 7 |  Ensure only experienced and licensed contractors are used. Ensure the contactor has visited the site and is aware of risks and completes companies internal risk assessment for each lift  Exclude all OTHR unnecessary staff and any onlookers within 100m of the lift area. If necessary install temporary fencing.  Throughout the lifting process the contractor is solely responsible for the lift and OTHR staff are not to be involved | No injuries to persons; No damage to rolling stock; All “near misses are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 1 | 2 | 3 |  |
| 21 | Rolling Stock | Moving Rolling Stock with heavy machines | 3 | 4 | 7 |  A detailed risk assessment is prepared prior to the move, including uncontrolled movements, braking procedures, safe working environment for the move excluding onlookers from the site.  Machines selected with appropriate safe working limit or other relevant parameters after consultation with appropriately qualified experts;  Competency of the machine operator confirmed  SWL for slings and D shackles confirmed  Non authorised persons are excluded from the work zone  Brakes are checked and serviced before commencement of movement  Experienced person to walk alongside rolling stock adjacent to brake handle.  Hauling speed to be at slow walking pace  Route inspected for hazards  A more in-depth risk register is developed specific to movement of rolling stock | No injuries to persons; No damage to rolling stock; No derailments; All “near misses or incidents are investigated within 14 days of occurrence, with all investigations having recommendations with 30 days. | 2 | 2 | 4 | Rolling Stock Manager |  |
| 22 | Runaway | Runaway of unattended construction or maintenance track machinery | 3 | 4 | 7 |  Prepare Safe Work Method Statement  Operators have the correct & current competency for the machine they are operating..  Hand brake is applied and/or wheels chocked when machine unattended. | No injuries to persons; No damage to track vehicles; No derailments; All “near misses or incidents are investigated within 14 days of occurrence, with all investigations | 2 | 2 | 4 | Infrastructure Manager |
| 23 | Rolling Stock Unload using tilt trailer | Unqualified and/or uninsured operator. Safely transport wagon from pick-up point to Oberon Unable to line up transport with rail Wagon may roll away when unloaded from transport Unable to unload wagon using the transports inbuilt mechanism | 3 | 5 | 8 | Independent check by OTHR on qualifications, currency and insurance Use of specialised rail transporter. Operator and assistant will guide transport into correct position. TM will ensure track is accessible Apply hand brake. Have wheel chocks ready. Clamp rail stop to down gradient side. Use a sleeper across the line if in doubt. Transport operation crew to perform unloading operation. OTHR to have contingency plan if wagon cannot be unloaded in the normal manner | No injuries to persons; No damage to track vehicles; No derailments; Adopt all controls - additional sleepers could be used between items of other rolling stock if necessary | 2 | 1 | 3 | Infrastructure Manager |

Likelihood –Severity Risk Ranking Matrix

Risk assessments are performed with the help of the matrix below that allows incident likelihood and consequences to be quantified. The matrix used by OTHR has been adapted from Australian Standard AS 4360 (2004) Risk Management and an ARTC model.

|  | Consequence (Cons) - NO Control/s |
| --- | --- |
|  | Not Significant 1 | Minor 2 | Moderate 3 | Major 4 | Extreme 5 |
| 5 ALMOST CERTAIN | L I K E L I H O O D (L’hd) | MEDIUM 6 | HIGH 7 | VERY HIGH 8 | VERY HIGH 9 | VERY HIGH 10 |
| 4 LIKELY |  | LOW 5 | MEDIUM 6 | HIGH 7 | VERY HIGH 8 | VERY HIGH 9 |
| 3 POSSIBLE |  | LOW 4 | LOW 5 | MEDIUM 6 | HIGH 7 | VERY HIGH 8 |
| 2 UNLIKELY |  | VERY LOW 3 | LOW 4 | LOW 5 | MEDIUM 6 | HIGH 7 |
| 1 RARE |  | VERY LOW 2 | VERY LOW 3 | LOW 4 | LOW 5 | MEDIUM 6 |
| RATINGS IN ALL FIELDS Higher Numbers are an undesirable level. Risk Level is the sum of the Likelihood and Probable Effectiveness of Control/s | 1 Most Effective | 2 Very Effective | 3 Moderately | 4 Not Very | 5 Least Effective |
| RATINGS IN ALL FIELDS Higher Numbers are an undesirable level. Risk Level is the sum of the Likelihood and Probable Effectiveness of Control/s | 1 Most Effective | 2 Very Effective | 3 Moderately | 4 Not Very | 5 Least Effective |
|  | Probable Effectiveness of Control/s (PEC) |
|  | RISK LEVEL Very High - Unacceptable (Intolerable) 8 - 10 High - Prompt Action Required (Intolerable) 7 Medium - Proceed with Caution 6 Low - Plan for corrective action 4 - 5 Very Low - Acceptable 2 – 3 |