ACTION BY KEY: CEO= President, OM= Operations Manager, SM= Systems Manager, SEC= Secretary, PO= Public Officer, TM= Track Manager includes ATM= Assistant TM, FC= Finance Co-ordinator, TR= Treasurer, IM= Infrastructure Manager, IA= Internal Auditor, RM=Rollingstock Manager

Risks in OTHR operation: Unloading 4 Wheel Wagons - Tilt-tray   Affects objective: Safely unload wagons to TEMPORARY STORAGE BESIDE THE RAIL.
Document Date: 04/10/2009  Reviewed: 08/09/12	Drafted by:  SM         Assessed by: …………………..………

| Risk No. | Hazard What can go wrong? | Risk What could happen? | Inherent Risk | Controls How could it be fixed? | Residual Risk | ALARP | Finding: Issues? Problems? Adopt? | Action |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Lik. | Cons | Risk |  | Lik. | Cons | Risk | ? |  | By | When |
| 1 | IN TRANSIT - Tilt Tray Removal from Orange to Oberon - under control of contractor using a tilt tray vehicle. | Loss or damage to load. Accident in transit. Over-size dangers. | 3 | 5 | 8 | Independently checked by OTHR prior to departure Ensure appropriate permits and adequate insurance in place. | 3 | 5 | 8 | ? | Out of our control but carry out sufficient checks to reduce our liability. | CEO SEC | ASAP |
| 2 | UNLOADING Personnel encroach upon safety zone. | Injury to public, OTHR workers and unloading crew. | 2 | 5 | 7 | Briefing prior to start. Security barriers & crowd control if required. Evacuation point marked. | 1 | 2 | 3 | y | Combination of all controls. | CEO /tm /RM | Lift day |
| 3 | UNLOADING Unauthorised entry to safety zone. | Injury to intruder. | 2 | 5 | 7 | Safety zone is within locked yard area. | 1 | 3 | 4 | y | Adopt & ensure gates are closed where possible. | CEO /tm /RM | Lift day |
| 4 | UNLOADING Unloading crew hit by load. | Injury to crew. | 3 | 5 | 8 | Briefing prior to start. Clear hazards from work area. All personnel to remain at the side of the vehicle and never behind the load. Wear PPE. | 2 | 2 | 4 | y | Adopt all controls. | CEO /tm /RM | Lift day |
| 5 | UNLOADING Holes, Uneven surfaces Tripping hazards. | Trips, falls and injury | 4 | 3 | 7 | Fill holes. Level uneven surfaces. Remove all obstacles. | 2 | 2 | 4 | y | Adopt all controls. | CEO /tm /RM | Lift -1 week |
| 6 | UNLOADING Winch fails and wagon rolls off the truck. | Injury or death to crew. Damage to load or property. | 3 | 5 | 8 | No personnel to be behind the vehicle and load. Chains and dogs to be progressively removed. Winch to be checked for ability to hold load before final chain removal. | 2 | 4 | 6 | y | Adopt. Supervise unloading team. | CEO /tm /RM | Lift day |
| 7 | UNLOADING Locating onto earth surface. | Load may topple sideways. Injury or death to crew. Pinch points. | 3 | 5 | 9 | Check ground surface for stability. Briefing prior to start. Ensure unloading crew is standing sufficiently to one side to avoid crushing. Wear PPE including gloves and hard hat. | 1 | 3 | 4 | y | Adopt all controls. Relocate if ground surface unstable or soft. | CEO /tm /RM | Lift day |
| 8 | R/STOCK STORED Runaway due to uneven surface, missing chocks or restraints. | Damage to wagon. Injury to workers including crushing during movement. Damage to property. | 3 | 5 | 8 | Fit effective restraints using sleepers either side of the wagon. Apply wagon handbrake & repair if ineffective. | 1 | 1 | 2 | y | Adopt all controls. Gradient is 1:174 towards Albion St. | CEO /tm /RM | Lift day |

ACTION BY KEY: CEO= President, OM= Operations Manager, SM= Systems Manager, SEC= Secretary, PO= Public Officer, TM= Track Manager includes ATM= Assistant TM, FC= Finance Co-ordinator, TR= Treasurer, IM= Infrastructure Manager, IA= Internal Auditor, RM=Rollingstock Manager

SIGNATURE SHEET - Risk Assessment for: ………………………………………………………………….……. (brief description)
Risk Assessment associated with OTHR operation described above.                          Date of Operation: …… /……. /2…….

| Risk No. | Hazard What can go wrong? | Risk What could happen? | Inherent Risk | Controls How could it be fixed? | Residual Risk | ALARP | Finding: Issues? Problems? Adopt? | Action |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Lik. | Cons | Risk |  | Lik. | Cons | Risk | ? |  | By | When |
| ALL | As described above. | I have discussed and understand the risks. | I will implement the Controls described above to the best of my ability so that the Risk is managed so that it is AS LOW AS REASONABLY PRACTICAL. | Note any issues you have with the Risks, Management or Controls. |
| OPERATING CREW. The operating crew on the day are requested to sign this document indicating that they have READ and UNDERSTOOD the RISKS and CONTROLS associated with this operation. | NAME (Print) ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… | POSITION (Task) ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… | signature ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… | COMMENT ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. |