ACTION BY KEY: PR= President, OM= Operations Manager, SM= Systems Manager, SEC= Secretary, TM= Track Manager, IM= Infrastructure Manager, RM=Rolling stock Manager, TL=Team Leader, DR= Driver, OB= Observer

Risks in OTHR operation: Carriage Shed Construction     Affects objective: Safety issues during Carriage Shed Construction
Document Date: 11/09/12 	Drafted by:  Ian Davis         Assessed by: PR/TM……………..………

REFERENCE:  POL- 012 Working at Heights Policy

TB-016 Working near Moving Machinery

TB-004 Emergency Procedures

| Risk No. Hazard What can go wrong? Risk What could happen? Inherent Risk Controls How could it be fixed? Residual Risk Finding: Issues? Problems? Adopt? Action L’hd. Cons Risk L’hd. PEC Risk By When |
| --- |
| 1 | Working at Heights |
| 1a | Worker could fall | Death or Injury to worker. Death or injury to worker on ground | 3 | 5 | 8 | Worker must be wearing approved safety harness and be properly secured to safety line. If working from “cherry picker” or “Manbox” workers must be wearing safety harness properly secured to machine. Any work performed above 2m from the ground must comply with POL-012 Working at Heights. Worker on ground must be 5m or more from operating machine and be visible to the driver. | 2 3 2 | 2 2 2 | 4 5 4 | Adopt. Refer: POL-012 Working at Heights Risk is higher here as machinery is also in use. | tm TL IM | During operation |

| ACTION BY KEY: PR= President, OM= Operations Manager, SM= Systems Manager, SEC= Secretary, TM= Track Manager, IM= Infrastructure Manager, RM=Rolling stock Manager, TL=Team Leader, DR= Driver, OB= Observer Risk No. Hazard What can go wrong? Risk What could happen? Inherent Risk Controls How could it be fixed? Residual Risk Finding: Issues? Problems? Adopt? Action L’hd. Cons Risk L’hd. PEC Risk By When |
| --- |
| 1b | Falling Tools or Materials | Death or injury to worker on ground. Damage to materials or tools. Damage to equipment on the ground | 3 3 3 | 4 3 3 | 7 6 6 | Only tools and materials required for immediate use must be at height. Assistance must be provided to worker at height for difficult to handle tools or material. Worker on ground must be aware of worker above, be a min 5m from operating machinery and be wearing PPE including hard hats | 3 2 2 | 2 2 2 | 5 4 4 | Adopt Workers on ground must be briefed prior to work commening | TM TL IM | During operation |
| 1c | Environmental | Worker could slip due to wet conditions (dew or rain) Wind could cause loss of control of materials (roof sheeting etc) | 3 | 5 | 8 | Work must cease when environmental conditions changed and caused hazardous conditions. Worker would be wearing a Roof Safety Kit in case of sudden changes in environmental conditions. | 2 | 3 | 5 | Adopt Refer: TB-024 Working in wet environment | TM TL IM | During operation |
| 1d | Human factors | Worker can get fatigued and become careless. Worker can become cold in exposed position and drop materials or tools. | 3 3 | 5 5 | 8 8 | Team leader must observe and converse with worker intending to work at height to satisfy himself that the worker is not fatigued and can work safely at height. | 2 | 2 | 4 | Adopt Refer: TB-007 Fatigue Management | TM TL IM | During operation |

| ACTION BY KEY: PR= President, OM= Operations Manager, SM= Systems Manager, SEC= Secretary, TM= Track Manager, IM= Infrastructure Manager, RM=Rolling stock Manager, TL=Team Leader, DR= Driver, OB= Observer Risk No. Hazard What can go wrong? Risk What could happen? Inherent Risk Controls How could it be fixed? Residual Risk Finding: Issues? Problems? Adopt? Action L’hd. Cons Risk L’hd. PEC Risk By When |
| --- |
| 2 | Working on Scaffolding or work platform |
| 2a | Worker could fall | Death or injury Injury to worker on ground | 3 | 4 | 7 | Worker must be working no more than 2m from ground. Scaffold must have safety rail. Worker must not work outside of safety rail | 2 | 3 | 5 | Adopt Refer: POL-012 Working at Heights Policy | TM TL IM | During operation |
| 2b | Poor Scaffolding Assembly | Scaffold could collapse causing worker to fall and injury. Injury to workers on the ground | 3 | 4 | 7 | Scaffold must be checked before each day’s work begins. All workers on ground must wear PPE including hard hat. | 2 2 | 2 2 | 4 4 | Adopt | TM TL IM | Before and during operation |
| 2c | Environmental | Worker could slip due to wet conditions (dew or rain) Wind could cause loss of control of materials (roof sheeting etc) | 3 | 5 | 8 | Work must cease when environmental conditions change and cause hazardous conditions. . |  |  |  |  |  |  |
| 2d | Human factors | Worker can get fatigued and become careless. Worker can become cold in exposed position and drop materials or tools. | 3 3 | 5 5 | 8 8 | Team leader must observe and converse with worker intending to work at height to satisfy himself that the worker is not fatigued and can work safely at height | 2 | 2 | 4 | Adopt Refer: TB-007 Fatigue Management | TM TL IM | During operation |

| ACTION BY KEY: PR= President, OM= Operations Manager, SM= Systems Manager, SEC= Secretary, TM= Track Manager, IM= Infrastructure Manager, RM=Rolling stock Manager, TL=Team Leader, DR= Driver, OB= Observer Risk No. Hazard What can go wrong? Risk What could happen? Inherent Risk Controls How could it be fixed? Residual Risk Finding: Issues? Problems? Adopt? Action L’hd. Cons Risk L’hd. PEC Risk By When |
| --- |
| 3 | Working with Mechanised Equipment |
| 3a | Excavator colliding with people or equipment | Death or injury to workers. Damage to equipment. Damage to excavator so that it is no longer available for use | 3 | 6 | 9 | Brief all workers on dangers. Remove all unnecessary workers from worksite Ensure all workers wear PPE. Ensure experienced and qualified operator | 2 | 2 | 4 | Adopt Brief using TB-016 Working near Moving Machinery | TM IM TL | Before and during operation |
| 3b | Use of forklift and Certified “Manbox’ | Death or injury to workers Damage to equipment. Worker falling from “Manbox” when elevated. Overloading Forklift becoming bogged in soft ground. | 3 3 2 2 3 | 6 5 6 5 5 | 9 8 8 7 8 | Brief all workers on dangers. Remove all unnecessary workers from worksite. Workers in “Manbox” to wear harness hooked to frame. Ensure experienced and qualified operator | 2 2 2 | 2 2 2 | 4 4 4 | Adopt | IM TL TM | Before and during operation |
| 3c | Use of hand tools | Breakage and injuring user. User injured by incorrect usage. Electric Shock hazard caused by incorrect or inattentive usage. | 3 3 3 | 5 5 5 | 8 8 8 | Brief workers before usage especially inexperienced users. Ensure that correct PPE is worn (Gloves, eye protection, suitable clothing) Ensure electrical supply leads are certified, in good condition and clear from damage when using hand tools. | 2 | 2 | 4 | Adopt | IM TL TM | Before and during operation |

ACTION BY KEY: PR= President, OM= Operations Manager, SM= Systems Manager, TM= Track Manager, IM= Infrastructure Manager , RM=Rollingstock Manager, DR = Driver , OB = Observer , TL= Team leader

SIGNATURE SHEET - Risk Assessment for: …Carriage Shed Construction     …
Risk Assessment associated with OTHR operation described above.                          Date of Operation:

| Risk No. | Hazard What can go wrong? | Risk What could happen? | Inherent Risk | Controls How could it be fixed? | Residual Risk | Finding: Issues? Problems? Adopt? | Action |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | L’hd. | Cons | Risk |  | L’hd. | Pec | Risk |  | By | When |
| ALL | As described above. | I have discussed and understand the risks. | I will implement the Controls described above to the best of my ability so that the Risk is minimised. | Note any issues you have with the Risks, Management or Controls. |
| OPERATING CREW. The operating crew on the day are requested to sign this document indicating that they have READ and UNDERSTOOD and ACCEPTED the RISKS and CONTROLS associated with this operation. | NAME (Print) ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… ………………………………………………… | POSITION (Task) ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… | signature ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… ………………………… | COMMENT ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. ………………………………………. |