|  | PO Box 299 Oberon NSW 2787 ABN 98 107 506 208 | Version | Author | Reviewed | Reference |
| --- | --- | --- | --- | --- | --- |
|  |  | A - Rev 2 | SM | SEC/TM | TB-026 |
|  |  | 29 Oct 2009 |
|  |  | Working With Cranes & Winches |

Work Area: ………………………………… 	Start Time: ………………………

Work Crew: ……………………………………………………………………………

Location: ………………………………… 		Date: …………………………….

Team Leader: …………………………… Presenter: …………………………………

Topic: Working With Cranes and Winches

- Mobile crane operations may present a risk of injury to persons from:

  - structural failure

  - crane overturning

  - contact or collision with other plant and structures

  - contact with overhead power lines - this can be very dangerous and all workers should be prepared to sound a warning if the operator does not see the lines

  - falling objects

- No person must drive or operate any crane or winch unless they have been properly trained and authorised to do so. Where necessary the appropriate certificate or license must be held and should be shown on the operator’s Certificate of Competency ID card. External contractors must furnish evidence of certification.

- If possible, avoid working near any moving crane. Never work in, or enter the “Swing Zone”.

- Keep other people clear of cranes and winching operations - watch out for your fellow workers.

- Keep unauthorised personnel well clear of the crane or winch.

- Wear appropriate PPE including Hard Hat if closer than 5m from the edge of the Swing Zone. 
The Swing Zone is a circular area, the radius of which is measured from the centre of the machine to the outside edge of the implement or gripped object when the machine is at full extension.

- If other machinery is nearby, designate a “spotter” to observe & control traffic movement.

- If possible, erect safety barriers and warning signs around operating cranes or winches.

- Winches pose a particular risk if the rope or chain breaks. Make sure all workers are outside the radius of the length of exposed cable should it break.

- Keep all personnel clear of the danger zone created by potential movement of the load should the rope or chain break. (Don’t stand behind the load).

- Any QUESTIONS or COMMENTS? 
The Presenter must record any questions or comments on the back of this form

Please sign that you have attended and that you understood the content of this meeting:

| Name | Signature | Name | Signature |
| --- | --- | --- | --- |