|  | PO Box 299 Oberon NSW 2787 ABN 98 107 506 208 | Version | Author | Reviewed | Reference |
| --- | --- | --- | --- | --- | --- |
|  |  | A - Rev 1 | SM | SEC/TM | SOP-001 |
|  |  | 23/09/2016 |
|  |  | Section Car (TMV) Operation |

STANDARD OPERATING PROCEDURE.

SECTION CAR

Any section car used will be operated subject to the conditions and definitions specified below.

- Only FINANCIAL MEMBERS of Oberon Tarana Railway Inc (OTHR) may drive or travel on the Section Car. The driver must be qualified to operate the section car.

- All crew members must wear appropriate PPE.

- The Section Car is only to be operated for its intended  purpose.

- Operations will be carried out between SUNRISE and SUNSET only.

- WRITTEN AUTHORITY to move the Section Car must be obtained by the qualified driver prior to checking the section car  (F-044 Authority to operate).

- When the driver has the signed Authority he/she will take possession of the Staff.

- The Authority will specify where and when the section car is to be used.

- The authorised driver will carry out a Daily Section Car Check (F-045) to satisfy (in writing) that to section car is safe to operate.

- Heavy equipment must be stowed in a safe manner which prevents injury to passengers and crew should the section car stop suddenly or be involved in an accident.

- The number of the operation crew (including the driver) shall at no time exceed the displayed operating personnel numbers.

- The authorised driver will use the Section Car to complete the required task in a safe manner and in the shortest possible time.

- Maximum speed of the Section Car will be as stated in the Authority.

- The horn and safety beacon must be tested before operations commence and the safety beacon must be ON during all operations.

- The Section Car must display the red flag when the car is stationary.

- It is the responsibility of the authorized driver or designated crew member to set any points encountered to the correct setting prior to the Section Car reaching the point.

- The Section Car is NOT to be used as a shunting locomotive.

- The Section Car can, subject to the approval of the Operations Manager, tow a light weight trailer. The laden weight of the trailer is to be less than the aggregate weight of the section car

- No passengers are to be carried at any time on a trailer.

Definitions:

SECTION CAR: a light weight  wheeled maintenance car which can be lifted onto the rail line. It is normally powered by a small internal combustion engine.

AUTHORIZED SECTION CAR DRIVER: a financial member of OTHR who has completed an OTHR training course for driving a section car. The driver must carry a current, certificate (card) indicating that satisfactory qualifications are held.

DANGER ZONE: everywhere within 3m horizontally from the nearest rail and any distance above or below this 3m, unless a safe place exists or can be created.